## Slide 1
PROGRESS REPORT · 28/09/2026
EmoTune
The Mood Music Box
An emotion-aware music recommender running on a Raspberry Pi
Group 6 Members: Nguyễn Đức Vinh, Hoàng Tuấn Phát, Phạm Thế Vỹ Supervisor: Nguyễn Trọng Kiên
Notes: Good morning, teacher and everyone. We are Group 6, and today we present EmoTune, a mood music box. It is a small device running on a Raspberry Pi that looks at your face, recognizes whether you are happy or sad, and plays music to match. The more you use it, the better it understands your taste. At the end, we will show a live demo on the real device.

## Slide 2
PART 1 · INTRODUCTION
Problem & Idea
Finding music that fits your mood means searching and picking it yourself — tedious, especially when you are tired or sad.
THE OLD WAY
Open app → search → pick
EMOTUNE
Sit down → music just plays
THE IDEA
Detects emotion from your face
Plays matching music by itself
Learns your taste from how you listen, no like button needed
Sits in your room like an appliance, no computer needed
02 / 10
Notes: It starts with a familiar problem: when you want music that fits your mood, you have to open an app, search and pick songs yourself, which is tiring, especially when you already feel tired or sad. With EmoTune, you just sit down and the music plays. Our idea has four parts: the device recognizes your emotion from your face, plays matching music by itself, learns your taste from how you listen without any like button, and sits in your room like an appliance, with no computer needed. Since this is a human–computer interaction course, our goal is simple: the user does as little as possible, and the machine takes the initiative.

## Slide 3
PART 1 · INTRODUCTION
System Architecture
Webcam C270
Speaker Bluetooth
RASPBERRY PI 5
mp3
React frontend
:5173
camera, music playback
Backend Node.js
:8080 · Express
recommends, stores history
AI Flask
:5000 · PyTorch
emotion recognition
GPIO service
:5001 · gpiozero
LED and buttons
PostgreSQL
songs, preference scores, mood history
One job per block: if LED/buttons fail, music keeps playing
LED + buttons
Hardware: Raspberry Pi 5 · Webcam Logitech C270 Bluetooth speaker · RGB LED + 2 push buttons
03 / 10
Notes: Everything runs on a Raspberry Pi 5, split into four software blocks. The webcam feeds the React frontend, which sends a photo to the Node.js backend. The backend asks the AI block, written in Flask and PyTorch, to recognize the emotion. It reads and writes PostgreSQL, where we store songs, preference scores and mood history, then returns an mp3 that the frontend plays on a Bluetooth speaker. A small GPIO service controls the LED and the buttons. We deliberately gave each block one job, so if the LED or buttons fail, the music keeps playing.

## Slide 4
PART 2 · HOW IT WORKS
How It Works
01
02
03
04
05
06
Press button 1 → start
white LED blinks = camera is on
Every 3 s take a photo
AI detects the emotion
Pick a song for the mood
camera off, music plays, LED changes color
Listen fully or press
button 1: next button 2: pause
Measure % of song played
→ add / subtract points
Song ends → scan again
camera on, back to step 2
LOOP: SONG ENDS → SCAN AGAIN
Fully automatic
Camera is off while music plays → saves resources, protects privacy, no junk data
04 / 10
Notes: This is one full cycle of use. The user presses button one to start, and a blinking white light shows the camera is on. Every three seconds the system takes a photo and the AI recognizes the emotion. Once a song is chosen, the camera turns off, the music plays and the LED switches to the color of that emotion. The user can listen to the end, press button one for the next song, or button two to pause. The system measures how much of the song was actually played and adds or subtracts points, then scans again when the song ends. The loop is fully automatic, and turning the camera off while music plays saves resources, protects privacy, and avoids logging junk data every three seconds.

## Slide 5
PART 3 · HIGHLIGHTS
Song Recommendation
1
Filter songs by emotion
2
Skip the 3 most recently played
no immediate repeats
3
Rank by preference score
each song has its own score per emotion
4
Pick with a 65 / 35 split
Current library: 10 songs, 2 per emotion
ILLUSTRATIVE EXAMPLE · MOOD: HAPPY
SONG
SCORE
STATUS
Song A
+2.3
✓ picked
Song B
+1.0
ranked lower
Song C
—
just played → skipped
Illustrative data
PICK STRATEGY · UPGRADE (IN PROGRESS)
65%
35%
Exploit: top-scored song
Explore: new songs you may like
65% plays songs you already like, 35% explores new songs that fit your taste
05 / 10
Notes: Once the emotion is known, the backend recommends in four steps: filter songs by emotion, skip the three most recently played to avoid repeats, rank songs by a preference score kept separately for each emotion, and then pick. Today the system uses an eighty–twenty split; the upgrade we are coding changes it to sixty-five–thirty-five. Sixty-five percent of the time it plays the top-scored song you already like, and thirty-five percent of the time it explores new songs, but favors the ones that fit your taste. The table on the right is only an illustrative example. Our current library has ten songs, two per emotion.

## Slide 6
PART 3 · HIGHLIGHTS
Taste-Based Recommendation
Upgrade · designed, in development
Today, scores are stored per song only → finishing ballad A tells us nothing about ballad B.
3 WAYS TO UNDERSTAND A SONG
Audio
ALWAYS
AI analyzes the mp3: tempo, loudness, brightness, timbre → 17-number fingerprint
Tags inside the mp3
IF PRESENT
artist, genre (ID3) → auto-filled into empty fields, never overwrites
Manual labels
OPTIONAL
genre: ballad, pop, rap… works fine without them
TOTAL SCORE OF A SONG
Own score + 0.5 × similarity to songs you played + 0.3 × same artist + 0.3 × same genre
EXAMPLE
finished Ballad A (artist X) and Ballad B (artist Y)
Ballad C (unheard)
90% similar → preferred
EDM track (unheard)
20% similar → ranked lower
Emotion stays the main criterion — taste only ranks songs within that emotion
The 35% exploration favors new songs you may like → the more you listen, the sharper it gets
06 / 10
Notes: While testing, we found a limitation: scores are stored per song only, so finishing one ballad tells the system nothing about another ballad. So we designed a taste-based upgrade, which is now in development. The system understands a song from three sources. First, audio, which is always available: a script analyzes the mp3 for tempo, loudness, brightness and timbre and turns it into a seventeen-number fingerprint. Second, artist and genre tags stored inside the mp3, when present. Third, optional labels the team can add by hand. A song's total score is its own score, plus zero point five times its similarity to songs you have played, plus zero point three for the same artist and zero point three for the same genre as songs you liked. For example, after finishing two ballads, an unheard ballad that sounds ninety percent similar is preferred, while an EDM track that is only twenty percent similar is ranked lower. Emotion stays the main criterion; taste only ranks songs within that emotion, and the more you listen, the sharper the recommendations get.

## Slide 7
PART 3 · HIGHLIGHTS
Learning from Listening
We measure the seconds actually played — skipped parts don't count
< 40%
40–80%
≥ 80%
−1
+0.3
+1
0%
40%
80%
100%
Skipped before 40% not a match
In between partly listened
Played ≥ 80% liked
No like button — listening behavior is the feedback
Scores are stored under the emotion used to pick → next time, fully played songs come first
Suggested by our supervisor last session — now implemented
07 / 10
Notes: So where do the scores come from? From listening behavior itself. The system measures the seconds actually played, not the parts you skip. If you skip before forty percent, the song loses one point because it is not a match. If you play eighty percent or more, it gains one point. Anything in between gains zero point three. That means no like button is needed: listening behavior is the feedback. Scores are stored under the emotion used to pick the song, so next time, with the same emotion, songs you listened to fully come first. This was our supervisor's suggestion from the last session, and it is now implemented.

## Slide 8
PART 3 · HIGHLIGHTS
Mood Care
CONDITION
Over 50% sad in the last day (or 3 days if used rarely) and currently sad/angry
happy
sad
mostly sad
Illustrative data · by day
ACTION
Switch to upbeat music
+ show an encouraging note
Not just following the mood — helping to lift it
08 / 10
Notes: The system does not just follow your mood; it also cares for it. It tracks the mood trend over the last day, or three days if the device is used rarely. If more than half of the readings are sad, and you are currently sad or angry, it switches to upbeat music and shows an encouraging note. The chart here is only an illustration of a long sad period. The idea is simple: playing sad songs forever to a sad person is not helpful, so the system actively changes direction to help lift the mood.

## Slide 9
PART 3 · HIGHLIGHTS
Hardware & Physical Interaction
Designed & coded · circuit in assembly
RGB LED
Off — not started
Blinking white — camera is on
Yellow — happy
Blue — sad
Red — angry
Purple — surprised
White — neutral
2 PUSH BUTTONS
Button 1
Start / Next song
Button 2
Pause / Resume
PIN MAP
COMPONENT
PI PIN
LED red (R)
GPIO17
LED green (G)
GPIO27
LED blue (B)
GPIO22
Button 1
GPIO5 ↔ GND
Button 2
GPIO6 ↔ GND
Each LED color goes through a 220–330Ω resistor
The Pi turns the project into a device — no screen needed
Edge AI: images are processed on the Pi, never sent online
Recognition < 3 s per scan
09 / 10
Notes: This is why we use a Raspberry Pi instead of a computer: the project is a device you interact with through a light and buttons, without looking at a screen. The RGB LED is off before starting, blinks white while the camera is on, so you always know when you are being watched, and while music plays it shows the emotion: yellow for happy, blue for sad, red for angry, purple for surprised and white for neutral. Button one starts or skips to the next song, and button two pauses or resumes. The table shows how they connect to the Pi's GPIO pins. Face images are processed right on the Pi and never sent online, and each recognition takes under three seconds. As for progress, the LED and button part is designed and coded, and tested with simulated pins; we are waiting for a breadboard to assemble the real circuit and will demo it next session.

## Slide 10
PART 4 · RESULTS
Demo & Results
ACHIEVED SO FAR
✓
Full loop runs on Pi 5
detect face → play → score → rescan
✓
Correctly logged to the database
mood history and feedback
✓
Demo anywhere
via the laptop hotspot
The full loop works on the Pi 5 — see it live →
LIVE DEMO
SCRIPT
1
2
3
4
5
Press button 1 → white LED blinks
Look at the camera
Music plays, LED shows the emotion color
Press button 1 → next song
Open the database to see the bad row just logged
SAMPLE mood_history TABLE
id
emotion
action
1
happy
suggested
2
happy
bad
3
sad
good
Illustrative data
10 / 10
Notes: So far we have achieved three things: the full loop runs on the Raspberry Pi 5, from detecting a face to playing, scoring and rescanning; the mood history and feedback are correctly logged in the database; and thanks to the laptop hotspot, we can demo anywhere. Now let us show you a live demo. I will press start, look at the camera, the music will play and match my emotion, then I will skip to the next song and open the database so you can see the bad row that was just logged. Thank you for listening, and we are happy to take your questions.